## Slide 1: MAŠINE ZA SABIJANJE TLA
Osnovna literatura:
B. Trbojević, Ž. Praščević: Građevinske mašine; Građevinska knjiga, Beograd, 1991 (korišćeno je izdanje 1991. godine, a mogu se koristiti i druga izdanja) str. 143-157

## Slide 2: MAŠINE ZA SABIJANJE TLA
svrha sabijanja:
  skraćenje vremena slijeganja nasutih slojeva
  povećanje nosivosti (nasutog ili prirodnog) tla
cilj sabijanja:
  smanjenje zapremine istiskivanjem vode i vazduha iz tla
generalna podjela u odnosu na dejstvo kojim se vrši sabijanje:
  statičkim dejstvom
    valjci
      glatki
      ježevi
      kompaktori
  dinamičkim dejstvom
    dejstvo vobracijama
      valjci sa dinamičkim dejstvom
      vibroploče
    dejstvo udarom - nabijači
      eksplozivni nabijači (“žabe”)

## Slide 3: MAŠINE ZA SABIJANJE TLA pregled povoljnosti primjene za različite materijale
vrsta zemlje
redosled mašina za savijanje prema povoljnosti upotrebe
optimalna vlažnost
granulisani materijal
vibracioni valjak
pneumatski valjak
glatki valjak
7-15%
granulisani materijal sa zemljom
vibracioni valjak
pneumatski valjak
glatki valjak
9-18%
fini čisti pijesak
pneumatski valjak
glatki valjak
9-15%
prašina
jež
pneumatski valjak
glatki valjak
10-20%
elastična prašina
jež
vibracioni valjak
pneumatski valjak
glatki valjak
10-35%
prašinasta glina, ilovača
jež
pneumatski valjak
glatki valjak
10-30%
elastična prašinasta glina, glina
jež
vibracioni valjak
pneumatski valjak
glatki valjak
20-35%
15-35%

## Slide 4: GLATKI VALJCI
Najstarije mašine za sabijanje, postojali su od izuma parne mašine
Mašine sa kontinualnim dejstvom
Sa dvije ili tri osovine i sa dva ili tri valjka
Više su za valjanje (odnosno obradu površine – glačanje peglanje), nego za sabijanje sa dubinskim dejstvom
Danas se uglavnom koriste samo za kolovozne konstrukcije na bazi ugljovodonika (bitumena)
Potrebna težina se postiže balastom (voda, pesak)

## Slide 7: VALJCI SA OVČIJIM NOGAMA - JEŽEVI
Mašine sa kontinualnim dejstvom
Glatki valjci po čijem se obodu nalaze nožice
Po kvadratnom metru omotača se nalazi 10 do 12 nožica
Najbolji za zbijanje zemlje, posebno koherentne, odnosno za plastiče materijale koji zahtijevaju miješanje i zbijanje – glinena jezgra na nasutim branama
Potrebna težina se postiže balastom (voda, pesak) od 100-400 KN
Obično se koriste u tandemu
Mogu da budu samohodni i vučeni
Broj prelaza je od 10 do 12
Dužina nožica iznosi od 18 do 23 cm
Debljina sloja treba da bude ista kao dužina nožica, izuzetno 1,2 dužine nožica
Smatra se da je tlo nabijeno ako nožice ne prodru dublje od 2-3 cm u sljedećem prolazu

## Slide 8: JEŽEVI
Notes: http://www.bomag.com/world/en/products/soil-compaction/Single-Drum-Rollers-9-to-15-tons-%28Series-4%29/BW+211+D-4i:-4.html
<number>

## Slide 9: KOMPAKTORI - VALJCI SA PNEUMATICIMA
Mašine sa kontinualnim dejstvom
Vozilo sa nizom pneumatika na osovini
Bar dva reda pneumatika, koji se međusobno prekrivaju
Potrebna težina se postiže balastom (voda, pesak) težine od 50 do 1000 kN
Manji (lakši) se koriste za puteve, veći (teži) za puteve, nasute brane i aerodrome, najveći za aerodrome
Mogu da budu samohodni i vučeni (za aerodromske piste i nasute brane)
Znatno pokretljiviji od ostalih vrsta valjaka
Posebno pogodni za nekoherentna tla
Potreban poseban mehanizam za ravnomerno opterećivanje točkova
Broj prelaza 6-10 puta
efekat rada na sabijanju zavisi od :
  opterećenja po točku,
  geometrije (oblika) pneumatika i pritiska vazduha
  broja prelaza

## Slide 10: KOMPAKTORI - VALJCI SA PNEUMATICIMA

## Slide 11: VALJCI SA DINAMIČKIM DEJSTVOM
Mašine sa kontinualnim dejstvom
Potrebna znatno manja težina nego kod valjaka sa statičkim dejstvom
Male brzine kretanja
Mogu da zbijaju znatno deblje slojeve nego kod valjaka sa statičkim dejstvom
Mogu da budu samohodni i vučeni
Dobri za nekoherentno i slabo koherentno tlo
dubina dejstva veća kod nekoherentnog tla, a kreće se od 20-120cm
Postoje u svim varijantama - glatki, jež, kompaktori
Vibracije se postižu rotacijom ekscentričnog tega
Za optimalno zbijanje potrebno odrediti adekvatnu amplitudu i frekvenciju oscilovanja

## Slide 12: VALJCI SA DINAMIČKIM DEJSTVOM

## Slide 13
Sistem regulisanih vibracija
VARIOCONTROL
Notes: sa sajta http://www.bomag.com/mobile/variocontrol/pdf/PRE104006_0811.pdf
BOMAG precision: How does VARIOCONTROL work? Only BOMAG produces vibration using directed oscillation with the VARIO exciter system in the drum. The exciter consists of counter-rotating eccentric weights. Individual centrifugal forces overlap due to counterdirectional rotation, so that the resulting force is only effective at one level. This generates directed vibration: the direction of vibration is changed by re-orienting the entire exciter unit. The drum can vibrate vertically or horizontally, or at any angle in between. Changing the direction of vibration is equivalent to changing the amplitude and with it the compaction energy introduced into the ground. Two acceleration transducers continuously measure the movement of the drum on the soil to calculate the optimum amplitude. This signal is then used to calculate the dynamic soil stiffness „EVIB“ in MN/m2 . If the dynamic stiffness of the soil – in other words the compaction – increases, the ground contact force will also increase. The movement of the drum changes and is recognised by the sensors. Optimum amplitude is calculated and the system adjusts in micro-seconds using these measurements.
Automatically better compaction: the automatic function With VARIOCONTROL automatic mode the driver selects a target EVIB value in MN/m2 . EVIB has a direct correlation to EV1 and EV2 in the plate load test. The automatic system continuously compares current results with the target value. If the variation is large, the system automatically uses high amplitude. This produces quick results and high efficiency especially at the beginning of compaction. The amplitude is reduced as the values approach the target. This gives uniform compaction over the entire area, even when initial conditions are not homogenous. The automatic system also avoids over-compaction, which can loosen the surface and destroy the soil structure. Once the target value has been achieved, or when no further compaction is possible, the driver is informed through the display and unnecessary passes are avoided.
<number>

## Slide 14
Asphalt Manager + BOMAG GPS System
Surface covering compaction control on asphalt layer
GPS receiver
GPS reference station
Roller PC for data managing and graphical representation of roller position and stiffness values
Position accuracy: better than 10 cm
CAD based evaluation program
Notes: https://www.ltrc.lsu.edu/asphalt/pdf/Intelligent%20Compaction.pdf
<number>

## Slide 15: UČINCI VALJAKA
Ne koristi se kp
Širina valjka B je jednaka širini trake
Brzina V, debljina sloja d i broj prelaza n se određuju opitom na opitnoj dionici da bi se postigla optimalna zbijenost

## Slide 16: VIBROPLOČE
Mašine sa kontinualnim dejstvom
Ploče, na kojima se nalazi motor i mehanizam za obezbeđenje vibracija
Nemaju mehanizan za samostalno kretanje, ali se lako mogu pomerati tokom rada, pošto vibriraju
Posebno pogodne na mjestima koja su teško pristupačne valjcima

## Slide 17: VIBRONABIJAČI – “Žabe”
dejstvo udarom
imaju sopsveni pogon koji omogućava njihovo poskakivanje
dobri za teško pristupačna mjesta

## Slide 18: UČINCI VIBROPLOČA
Ne koristi se kp
Širina ploče B je jednaka širini trake
Brzina V, debljina sloja d i broj prelaza n se određuju opitom da bi se postigla optimalna zbijenost